## Slide 1
September 2018
IP Camera Signal Transmission
XCU Concept, XCU UXF, including DirectIP and DirectIP+
Changing the landscape for LIVE remote productions

## Slide 2: Agenda
Why going to IP
IP Fundamentals
XCU - Camera base station with cradle solution
XCU UXF - Next generation camera base station
Why looking for remote productions
DirectIP - Camera signal transmission over IP
DirectIP+ - Remote production over IP networks

## Slide 3: Why going to IP

## Slide 4: Why going to IP – It’s a time of multiple changes
…from HD to 4K to 8K
…from SDR to HDR
…from a single to multiple distribution channels
…and many other things to come

## Slide 5: Why going to IP – The acceleration of format changes
Creating challenges with facility costs, speed of deployment & training
Black & white
Color
1934
1972
HD
2002
4K
2016
8K
2020
38 Years
30 Years
14 Years
4 Years

## Slide 6: Why going to IP - What can IP do for you?
 | Video, audio, metadata, intercom
 | Multiple signals per cable
 | Bi-directional signals
 | Format & frame rate agnostic
 | New workflow models
 | Fast service launches
 | Easier, linear scaling (non-blocking)
 | Dynamic infrastructure ease of upgrades

## Slide 7: Why going to IP – Summary for live applications
IP…
…add flexibility
…enables improved workflows
…support dynamic infrastructures
…delivers fully future proof solutions
IP help to better cope with the challenges in live broadcast applications
Notes: But what if you could leverage the strengths of data centers …

## Slide 8: IP - Fundamentals

## Slide 9: IP - Fundamentals – AIMS roadmap

## Slide 10: IP - Fundamentals – SMPTE 2022-6 signal structure
SMPTE 2022-6 is like converting “SDI into the IP world”
ANC Data
Video
IP & 2022-6 Header
All “info” available in the SDI stream about video, audio, etc.
Audio & I-Com
SDI - World
IP - World
SDI Stream
SMPTE 2022-6 Stream

## Slide 11: IP - Fundamentals – SMPTE 2022-6 signal flow
SMPTE 2022-6 carry all the different signals into one IP stream
  All signals are always in sync
    Therefore an optimized solution e.g. interconnecting two sites (or to transmit signals between camera head and XCU)
  Any processing require to “un-pack” and “re-pack” the IP stream

## Slide 12: IP - Fundamentals – SMPTE 2110 signal structure
SMPTE 2110 for more efficient use of IP signal structure
Video / RFC 4175
All “info” available in the stream about video, audio, etc.
Audio / RFC 3190
SMPTE 2022-6
SMPTE 2110
SMPTE 2022-6 Stream
SMPTE 2110 Streams
-20
-30
-30
-40
SDP
I-Com / RFC 3190
ANC Data
SMPTE 2110 compared to SMPTE 2022-6
has reduced bandwidth by only
transmitting active part of video,
e.g. blanking is not transmitted
Description about video, audio, etc. necessary for the “receivers” to understand the content of the IP-packages
(Static configuration Info)
Session Description Protocol
IP header
Video
Audio
SDP-file
ANC data

## Slide 13: IP - Fundamentals – SMPTE 2110 / Why SDP File?
Info required for receivers to “understand” the content of IP packages
  Without the SDP file the receiver don’t know which essences belong together
2110 -20
2110 -30
2110 -40
?
IP-link
2110 -20
2110 -30
2110 -40
SDP
+
IP-link
Automatic set-up via SDP
Generated by IP source
IP destination
IP source

## Slide 14: IP - Fundamentals – SMPTE 2110 signal flow
SMPTE 2110 carry the different signals as separate essence in IP
  All signals are available as separate essences making the individual use of any signal easier and more efficient it is optimized for in-house workflows
  Optimized bandwidth efficiency by only carry required data's

## Slide 15: XCU - Camera base station with cradle solution

## Slide 16: XCU - Camera base station with unique cradle solution
Additional camera base stations can be installed in seconds
  Support all LDX Series camera in all operational modes
  Memory in the cradle will automatically load the settings from the environment

## Slide 17: XCU – What the unique cradle solution can do for you
The cradle…
…add flexibility
…enables improved workflows
…support dynamic infrastructures
…delivers fully future proof solutions
The cradle help to better cope with the challenges in live broadcast applications
Notes: But what if you could leverage the strengths of data centers …

## Slide 18: XCU UXF - Next generation camera base station

## Slide 19: XCU UXF - And advanced UXF Cradle
Delivers an essential step towards a full IP live production solution
  Full Hybrid XCU with ALL signals available in baseband and IP creating maximum production flexibility
    Support of AIMS roadmap with full ST2110-10/20/30 and redundancy
    Support SMPTE 2022-6
  Support all production formats in IP as well as in base band
    Uncompressed 4K single speed or 4K TICO
    HD/3G with up to 6x speed
    Simultaneous SDR and HDR operation
    Wide color gamut

## Slide 20: XCU UXF - And advanced UXF Cradle
New cradle with additional 4x MSA compliant SFP+ slots
  Adding network redundancy
  Can be equipped with 10 Gb/s Fiber SFP’s or with 12G SDI SFP
    12G SDI with single BNC or dual HD-BNC
Redundant IP Network
2x 10Gb/s
Main IP Network
2x 10Gb/s
12G SDI

## Slide 21: XCU UXF - ALL signals available in baseband and IP
XF Fiber
Baseband Connections
Supporting 4K, 3G, HD, HDR, returns, monitoring, reference, prompter
Supporting Audio (Analog / SDI / AES/EBU)
Supporting I-Com (2-wire / 4-wire)
Supporting Tally
Supporting Camera Control (C2IP)
Supporting GPIO / data
4x 10Gb/s IP Connections
2x main + 2x redundant
Supporting 2022-6 and SMPTE 2110
Supporting 4K, 3G, HD, HDR, returns, monitoring, reference (PTP), prompter
Supporting Audio (AES67)
Supporting I-Com (AES67)
UXF Cradle

## Slide 22: XCU UXF - Most seamless transition from base band to IP
  Different steps available during evolution to IP
  Advantage: Low risk, keep using proven infrastructure
  SDI for main signals and back-up
  SDI is still used for main and back-up as “test” with IP in parallel (no risk)
  When confident with IP, change-over to IP for main and SDI as back-up
  Make use of full IP advantage also for redundant IP path
  Everyone can migrate from base band to IP at their own speed!
Main
Back-up / Redundant
SDI
SDI
SDI
SDI
IP (test)
IP
SDI back-up
IP
IP
Redundant
A
B
C
D
Time
IP SDI / Baseband
A
B
C
D

## Slide 23: XCU UXF – IP Media streams: SMPTE 2022-6
IP Network 10Gb/s
10Gb Ethernet
10Gb/s Ethernet
10Gb/s Ethernet
Main
2022-6
Monitor
2022-6
Ext 1 2022-6
Ext 2
2022-6
TP
2022-6
TP
Ext 1
I-Com (prog + prod + eng) de-embedded
Ext 2
Main Video : HD / 3G / 4K-Tico
Audio (1+2+3+4) embedded
I-Com (prod + eng) embedded
Monitoring Video : HD
Audio (1+2+3+4) embedded
I-Com (prod + eng) embedded
Multicast (+ IGMP)
Unicast
PTP (2059 ; Slave)
Multicast (+ IGMP)
Unicast
PTP (2059 ; Slave)
Audio / I-comm
Audio (1+2+3+4 ; 2110-30 ; L24)
I-Com (prod + eng ; 2110-30 ; L24)
I-Com (prog + prod + eng (+2nd prog) ; 2110-30 ; L24)
Main 3G
2022-6
4K main in 3G
Audio (1+2+3+4) embedded
I-Com (prod + eng) embedded
IP streams can be switched on/off
Audio / I-comm
Audio (1+2 ; 2110-30 ; L24)

## Slide 24: XCU UXF – IP Media streams: SMPTE 2110
TP
Ext 1
Ext 2
Main Video : HD / 3G / 4K-Tico
Monitoring Video : HD
Audio (1+2+3+4 ; 2110-30 ; L24)
I-Com (prod + eng ; 2110-30 ; L24)
I-Com (prog + prod + eng (+2nd prog) ; 2110-30 ; L24)
4K main in 3G
IP streams can be switched on/off
Audio (1+2 ; 2110-30 ; L24)
RFC LIVE
Audio / I-comm
Audio / I-comm
RFC Mon
RFC HD
Ext 1
Ext 2
Ext 3 / TP
10Gb/s Ethernet
SDP
IP Network 10Gb/s
Multicast (+ IGMP)
Unicast
PTP (2059 ; Slave)
Multicast (+ IGMP)
Unicast
PTP (2059 ; Slave)
10Gb/s Ethernet

## Slide 25: XCU UXF – Overview of all IP connections
Camera
Camera Control
network
( C2IP )
OCP
MCP450
IP switch
10/100/1G
e.g. VSM Control
(XML command protocol )
IP trunk
10/100/1G
XF transmission
10G IP
(Hybrid Fiber cable)
MAIN
IP network
10G IP
REDUNDANT
IP network
10G IP
IP trunk
10/100/1G

## Slide 26: XCU – What the XCU UXF can do for you
The XCU UXF…
…add flexibility
…enables improved workflows
…support dynamic infrastructures
…delivers fully future proof solutions
The XCU UXF help to better cope with the challenges in live broadcast applications
Notes: But what if you could leverage the strengths of data centers …

## Slide 27: Why looking for remote productions

## Slide 28: Why looking for remote productions
At typical OB-van productions…
…much (expensive) equipment is „on the road“ for most of the time.
…and a lot of operational people need to travel too.

## Slide 29: Why remote production – Better efficiency

## Slide 30: Why remote production – Better efficiency

## Slide 31: Remote Production - Possible workflows
Traditional remote productions
+ Full flexibility
+ Adjustable bandwidth requirements
- IP gateway or dedicated network
multiplexing equipment required
- Difficult to set-up and maintain

## Slide 32: C2IP – IP based Camera Control Solution
The first camera control system fully based on open IP standards
  10/100BASE-T Ethernet / TCP/IP
  Layer 2
    For typical operation
  Layer 3
    For remote applications
    Managed by C2IP name server
    as option for the MCP 450
  LDX Connect gateway
    Embedded in the MCP 450
    Delivering an interface to
    third party control solutions
    via XML commands
    SDK available on request

## Slide 33: DirectIP - Camera signal transmission over IP

## Slide 34: DirectIP - XF Transmission 10Gb IP based
10Gb IP
IP Trunk
10/100/1G
Private Data
Analog Audio Stereo 24bits
Main Video
2022 5+6
Digital Audio Stereo 24bits
I-com Prod. Audio 16bits
I-com Eng. Audio 16bits
C2IP
Fiber A
10Gb IP
IP Trunk
10/100/1G
Private Data
I-com Eng. Audio 16bits
I-com Prod. Audio 16bits
Return
2022 5+6
I-com Prog. Audio 16bits
C2IP
Fiber B
Main ; 1 Channel SMPTE 2022-5+6
1080i50/59 = 1,8Gb
1080p50/59 = 3,4Gb
Return ; 1 Channel SMPTE 2022-5+6
1080i50/59 = 1,8Gb
1080i50/59 = 1,8Gb
C2IP + Private Data + I-com +
Analog Audio + Digital Audio =
~ 8Mb
IP Trunk =
0Mb (when not connected)
SMPTE Hybrid Fiber cable
incl. 2x single mode fiber
Fiber A
Fiber B

## Slide 35: DirectIP - XF Transmission over 10G IP network

## Slide 36: Remote Production - Possible workflows
2. DirectIP
+ Highest performance
+ Max. flexibility / utilization of equipment
+ Only COTS hardware required
+ Easy to set-up and maintain
- High performance IP network required
- Typically limited to campus installations

## Slide 37: DirectIP - Why the XCU is required still (today)…
…the XCU generate all the base band signals
…the XCU deliver redundancy
…the XCU does some conversions / processing of UHD / HD
…the XCU provide the AnyLightXtreme flicker reduction
SMPTE hybrid Fiber connection for camera including power
4x SFP+ ports for extended IP connectivity
scalable from “just” video to a full IP production
All the traditional baseband connectivity from regular XCU’s while transitioning to IP

## Slide 38: DirectIP – Use case “Cloud” production at NEP-NL
NEP “owns” the fiber network
Redundancy in the network (Spine-Leaf)
VSM Control for secure switching between studio’s
Separate VLAN for all cameras
Production site 1
Production site 2
Production site 3
Centralized control room

## Slide 39: DirectIP – Use case MySports Switzerland
Playout center near Zürich with remote-connection to TV-Studio in Rossens for French program
  Distance between the two sites approximately 200km
Studio Rossens for French program
Studio Zürich for German and Italian program
100 Gigabit
Redundant single mode fiber
UPC Data Highway

## Slide 40: DirectIP - Overview of the bandwidth requirements
Bandwidth requirements depend on the operational mode
  Transmission through 10G SFP+ modules (Single Mode) in IP switches
  Plus in addition for Audio, I-comm, C2IP, Private date, etc. = about 8Mb
Example: 5x camera running in 1080i fit into 10Gb bandwidth

## Slide 41: DirectIP - Overview of the bandwidth requirements
Bandwidth requirements depend on the operational mode
  Transmission through 10G SFP+ modules (Single Mode) in IP switches
  Plus in addition for Audio, I-comm, C2IP, Private date, etc. = about 8Mb
Example: 5x camera running in 1080i fit into 10Gb bandwidth

## Slide 42: DirectIP – What the Direct IP solution can do for you
DirectIP…
…add flexibility
…enables improved workflows
…support dynamic infrastructures
…delivers fully future proof solutions
DirectIP help to better cope with the challenges in live broadcast applications
Notes: But what if you could leverage the strengths of data centers …

## Slide 43: Direct IP+ - Remote production over IP networks

## Slide 44: From DirectIP to DirectIP+
All applications where high performance IP infrastructures are available can benefit from the multiple advantages DirectIP offers.
  Higher flexibility, better utilization of equipment, lower operational cost, etc.
DirectIP is an ideal solution for Studio’s, Sports venues, Universities, etc.
  And any other application where 10G IP fiber infrastructures are available.
… but what if 10Gb bandwidth is not available? ... E.g. only 1Gb?
Is it possible to “compress” the video part only?

## Slide 45: Solution – DirectIP with additional Plus functionality
Compress the video streams, so they fit into smaller bandwidth
Keep IP connection for Audio, I-com, C2IP uncompressed (8Mb trunk)
e.g.

## Slide 46: DirectIP+ - System overview with Net Insight’s Nimbra
1 Gb/s
Full duplex
Wide area network
Notes: Service isolation und 93% der auslastung auf dem link
Full stream separation and service isolation end to end
End to end resource allocation to avoid overprovisioning
Traffic shaping and admission control at ingress protect the overall QoS
Full synchronization mechanisms between the different streams
Belgium use case from Cross point at NEP 10G Network
8ms für uncompressed
90 ms für compressed with Direct IP Plus
Wir sehen manchmal auch einen mix der signale
Quality of Service
For professional media services
Service Isolation
For security and predictability
Timing - Sync
PTP and synchonization support
High availability
Too meet strong SLAs
Service Provisioning
Without additional traffic engineering
Monitoring
Per service health monitoring
and SLA compliance
Challenge
Professional media services defines the concept “mission critical”. Customers demands highest possible availability for their services.
Solution
Nimbra MSR has a large palette of availability functions, from fast service re-routing to service specific redundancy, to fit the purpose and wallet. ETS specifically has Hitless 1+1 protection for any streaming service (not only SMPTE 2022) as an option.
ETS Benefits
ETS Hitless 1+1 enables protection for any streaming service against both intermediary loss (burst and random packet loss) as well as complete connection failures. Especially useful together with “smart SFPs” that for instance converts SDI, or even TDM services as E1/E3, to IP/Ethernet. ETS Hitless 1+1 enhances the value of these services.
Kunden besuch
AES-67

## Slide 47: DirectIP+ - Specifications with Net Insight’s Nimbra
Net Insight Nimbra SFP Video Access Module J2K
  10 to 250 Mbps for 1080i
  10 to 500 Mbps for 1080p
1080i with J2K @ 160 Mbps…
1080p with J2K @ 320 Mbps…
…seen as visible lossless quality
  Approximately 10x less bandwidth
  required compared to uncompressed
Overall latency - except IP network – approximately 100msec

## Slide 48: Remote Production / Possible workflows
3. DirectIP+ / DirectIP funtionality over low bandwidth IP networks
+ Full flexibility
+ Adjustable bandwidth requirements
+ Best utilization of equipment
+ Transport over any underlying infrastructure
- Dedicated network multiplexing
equipment required

## Slide 49: Summary Remote production over IP networks

## Slide 50: Remote Production - Possible workflows
Traditional remote productions
3. DirectIP+
+ Full flexibility
+ Adjustable bandwidth requirements
+ Best utilization of equipment
+ Transport over any underlying infrastructure
- Dedicated network multiplexing
equipment required
+ Full flexibility
+ Adjustable bandwidth requirements
- IP gateway or dedicated network
multiplexing equipment required
- Difficult to set-up and maintain
2. DirectIP
+ Highest performance
+ Max. flexibility / utilization of equipment
+ Only COTS hardware required
+ Easy to set-up and maintain
- High performance IP network required
- Typically limited to campus installations